## Slide 1: Startup Weekend Aix-Marseille
October, 28-31th, 2016

## Slide 2: Tools
Arduino IDE
  Based on Processing (Java) + ARM GCC
  Application based on Arduino API + libraries
Atmel Studio
  Based on Microsoft Visual Studio CLI + ARM GCC
  Application based on Atmel Software Framework
Available base kits in Arduino context
  AVR ATMEGA328P Xplained mini
  SAMD21 Xplained Pro + Xplained extensions
  SAMW25 Xplained Pro + Xplained extensions
Available base kits in Atmel Studio context
  SAMD21 Xplained Pro + Xplained extensions
  SAMW25 Xplained Pro + Xplained extensions
  SAM4E Xplained Pro + Xplained extensions

## Slide 3: Kits usable with Arduino IDE
The following kit descriptions correspond to their use in Arduino IDE context.
The AVR ATMEGA328P Xplained mini is pin to pin compatible with Arduino Uno, thus benefits of all efforts done on this platform. The Board Support Package (BSP) is provided through the Arduino IDE Boards Manager and available on Arduino servers.
The SAMD21 Xplained Pro and SAMW25 Xplained Pro are respectively software compatible with Arduino Zero and MKR1000. They share a BSP available on Github which needs to be manually installed, as explained in the repository Wiki companion.

## Slide 4: AVR atmega328p Xplained mini
Arduino pinout view

## Slide 5: SAMD21 Xplained Pro
Arduino pinout view
A2
Ser2/RX
A3
D19
D9
D11
Wire/SCL
SPI1/MOSI
D8
D18
D10
SPI1/MISO
SPI1/SS
Ser2/TX
SPI1/SCK
Wire/SDA
A0
Ser1/RX
A1
D17
D5
D7
Wire/SCL
SPI/MOSI
D4
D16
D6
SPI/MISO
SPI/SS
Ser1/TX
SPI/SCK
Wire/SDA
A4
Ser2/RX
A5
D21
D13
D15
Wire/SCL
SPI2/MOSI
D12
D20
D14
SPI2/MISO
SPI2/SS
Ser2/TX
SPI2/SCK
Wire/SDA
Arduino pins D2-D15 are pure GPIO. D16-D21 are GPIO and PWM.
LED0 is D2
SW0 is D3
Serial on Embedded Debugger

## Slide 6: SAMW25 Xplained Pro
Arduino pinout view
A0
Serial1
A1
D9
D5
D7
Wire/SCL
SPI
D4
D8
D6
SPI
SPI
Serial1
SPI
Wire/SDA
WiFi on SPI1
LED0 is D2
SW0 is D3
Arduino pins D2-D7 are pure GPIO. D8-D9 are GPIO and PWM.
Serial on Embedded Debugger
Notes: Pinout ref: https://github.com/AtmelUniversityFrance/atmel-samd21-xpro-boardmanagermodule/blob/master/module/variants/atmel_samw25_xpro/variant.cpp

## Slide 7: Kits usable with Atmel Studio
The following kit descriptions correspond to their use in usual industrial context.
These kits are usually used in a product evaluation context and even if their design is a working one, they shouldn’t be considered as reference design.
The Xplained Pro platform is an Atmel ecosystem gathering the kits hardware, the according documentation and as much as possible software examples.
Basic or applicative applications are made available through Atmel Software Framework (ASF). ASF is preferred used with the free Atmel Studio but also with any other development environment via its standalone delivery.
Some kits being appreciated by Open Source Community have been integrated to various projects according to their specific characteristics.
Atmel Xplained Pro platform

## Slide 8: Xplained Pro Extension header pinout

## Slide 9: SAM4E Xplained Pro
Atmel Studio/Software Framework pinout
PB03
PA22
PB2
PA15
PA24
PA11
PA03
PB14
PA025
PA16
PD25
PA14
PA13
PA21
PA12
PA04
Embedded Debugger
2Gb
NANDFlash (EBI)
SW0
(PA02)
2 x 512K
SRAM (SMC)
PC13
PA06
PA17
PD20
PD28
PE01
PA03
PD30
PD17
PD24
PD26
PA14
PA13
PA05
PA12
PA04
NC
PA06
NC
PD21
PE02
PD29
PA03
PD23
PB5
NC
PB4
PA14
PA13
PA05
PA12
PA4
Ethernet
CAN

## Slide 10: IO1 Xplained Pro
Extension pinout
1 | ID | 2 | GND
3 | Light Sensor | 4 | LP_out
5 | GPIO1 | 6 | GPIO2
7 | LED | 8 | LP_IN
9 | TEMP_ALERT | 10 | MicroSD Detect
11 | TWI_SDA | 12 | TWI_SCL
13 | UART_RX | 14 | UART_TX
15 | MicroSD SS | 16 | SPI_MOSI
17 | SPI_MISO | 18 | SPI_SCK
19 | GND | 20 | VCC
Light Sensor
Low pass filter (LP)
microSD card slot (SPI)
Temperature Sensor (TWI)
LED

## Slide 11: OLED1 Xplained Pro
Extension pinout
1 | ID | 2 | GND
3 | BUTTON2 | 4 | BUTTON3
5 | OLED DATA_CMD | 6 | LED3
7 | LED1 | 8 | LED2
9 | BUTTON1 | 10 | OLED RESET
11 | NC | 12 | NC
13 | NC | 14 | NC
15 | OLED SS | 16 | SPI MOSI
17 | NC | 18 | SPI SCK
19 | GND | 20 | VCC
LEDs
OLED Display (SPI)
Push Buttons

## Slide 12: PROTO1 Xplained Pro
Extension pinout
Internal Power In/External Power Out area
External Power Connector
Remapped Extension Connector
Power Connector
GND/VCC Area
Prototype Area

## Slide 13: ATWINC1500 Xplained Pro
Extension pinout
1 | ID | 2 | GND
3 | NC | 4 | NC
5 | WINC1500 RESET | 6 | WINC1500 WAKE
7 | NC | 8 | NC
9 | WINC1500 IRQ | 10 | WINC1500 CHIP ENABLE
11 | I2C SDA | 12 | I2C SCL
13 | UART RX | 14 | UART TX
15 | WINC1500 SS | 16 | SPI MOSI
17 | SPI MISO | 18 | SPI SCK
19 | GND | 20 | VCC
WINC 1500 Module
WINC 1500 DEBUG UART
WINC 1500 DEBUG (I2C)
Power Measurment Jumper

## Slide 14: References
Atmel Studio http://www.atmel.com/tools/atmelstudio.aspx#download
Arduino IDE https://www.arduino.cc/en/Main/Software
Atmel University France http://atmeluniversityfrance.github.io/
Atmega328p-xmini wiki https://github.com/AtmelUniversityFrance/atmel-avr-xmini-boardmanagermodule/wiki
SAMD21/W25-XPRO wiki https://github.com/AtmelUniversityFrance/atmel-samd21-xpro-boardmanagermodule/wiki

## Slide 15
© 2016 Atmel Corporation.
Atmel®, Atmel logo and combinations thereof, Enabling Unlimited Possibilities®, and others are registered trademarks or trademarks of Atmel Corporation or its subsidiaries. ARM®, ARM Connected® logo and others are the registered trademarks or trademarks of ARM Ltd. Other terms and product names may be the trademarks of others.
Disclaimer: The information in this document is provided in connection with Atmel products. No license, express or implied, by estoppel or otherwise, to any intellectual property right is granted by this document or in connection with the sale of Atmel products. EXCEPT AS SET FORTH IN THE ATMEL TERMS AND CONDITIONS OF SALES LOCATED ON THE ATMEL WEBSITE, ATMEL ASSUMES NO LIABILITY WHATSOEVER AND DISCLAIMS ANY EXPRESS, IMPLIED OR STATUTORY WARRANTY RELATING TO ITS PRODUCTS INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, OR NON-INFRINGEMENT. IN NO EVENT SHALL ATMEL BE LIABLE FOR ANY DIRECT, INDIRECT, CONSEQUENTIAL, PUNITIVE, SPECIAL OR INCIDENTAL DAMAGES (INCLUDING, WITHOUT LIMITATION, DAMAGES FOR LOSS AND PROFITS, BUSINESS INTERRUPTION, OR LOSS OF INFORMATION) ARISING OUT OF THE USE OR INABILITY TO USE THIS DOCUMENT, EVEN IF ATMEL HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES. Atmel makes no representations or warranties with respect to the accuracy or completeness of the contents of this document and reserves the right to make changes to specifications and products descriptions at any time without notice. Atmel does not make any commitment to update the information contained herein. Unless specifically provided otherwise, Atmel products are not suitable for, and shall not be used in, automotive applications. Atmel products are not intended, authorized, or warranted for use as components in applications intended to support or sustain life.

## Slide 16: Blynk.cc
Blynk is a Platform with iOS and Android apps to control Arduino, Raspberry Pi and the likes over the Internet.
It's a digital dashboard where you can build a graphic interface for your project by simply dragging and dropping widgets.
It's really simple to set everything up and you'll start tinkering in less than 5 mins.
Fast application prototyping

## Slide 17
http://atmeluniversityfrance.github.io/

## Slide 18
SAMD21/W25/R21 Arduino module/BSP
https://github.com/AtmelUniversityFrance/atmel-samd21-xpro-boardmanagermodule

## Slide 19
Link to this document
https://github.com/AtmelUniversityFrance/StartupWeekendAixMarseille_201610/blob/master/SWAM_october2016.pptx